## Slide 1
Braille-Based IoT Home Automation for
Multi-Disability Empowerment
SESHADRI RAO GUDLAVALLERU ENGINEERING COLEGE
(An Autonomous Institute permanently affiliated to JNTUK , Kakinada)
Department of Electronics and Communication Engineering
Batch Members:
N. Manikanta Raghava — 23485A0424
M. Jahnavi — 22481A04F5
N. Venkata Siva Prasanth — 23485A0423
Md. Habeeb Pasha — 22481A04F8
Guided by:
Mr. V. Vittal Reddy
(Associate Professor)
Batch No : C5

## Slide 2
Objectives of the Project Work
Develop a low-cost, accessible Braille-based IoT system that empowers visually and speech-impaired individuals to control home appliances independently, providing real-time confirmation through haptic feedback and audio signals to ensure accuracy and ease of use.
Implement an intelligent emergency alert system that detects hazards like fire and instantly notifies caregivers via Blynk IoT cloud push notifications ensuring continuous safety and reliability during critical situations.

## Slide 3
Abstract of the Project Work
This project presents a Braille-based IoT home automation system designed to assist visually and speech-impaired individuals. Built on ESP32 microcontrollers, the system employs a custom persistent TCP protocol to transmit commands from a portable six-dot Braille keypad to a central appliance controller. Accessibility is ensured through simultaneous haptic (vibration) and auditory feedback for the user, while an SSD1306 OLED display provides visual status for caregivers. Additionally, the system integrates flame sensors and Blynk IoT connectivity to provide real-time safety alerts, offering a secure, reliable, and inclusive alternative to conventional smart home controls.

## Slide 4
Hardware Wiring Diagram
Remote Module

## Slide 5
Hardware Wiring Diagram
Appliance Control Module

## Slide 6: Flow chart
Power ON
Initialize sensors & Wi-Fi
Read inputs
Send ACK or STOP
Send appliance command
Is Feedback Received from TCP
Play Feedback
Power ON
Initialize sensors, Wi-Fi & Display
Listen TCP for commands
Emergency alert
Decode command
Is Command Received
Update display
Execute command & give Feedback
Is Flame detected
Monitor Flame sensor
Braille Keypad Module
Appliance Control Module
Valid Braille Input
Emergency
Yes
Yes
Yes
No
No
No
‘F’ fire alert
feedback pattern →
S/E/C/W
feedback pattern →

## Slide 7
Module Communication & Braille Recognition
System Connectivity
Network Topology
Operates on a Master/Slave model where the Remote Module (TCP Client) connects to the Appliance Module (TCP Server) on Port 7890 .
Dual-Mode Wi-Fi
Utilizes WIFI_AP_STA mode to allow either connection via a router or direct peer-to-peer (AP) connection.
The Braille Recognition Engine
The system uses bitwise logic to convert physical inputs from a 6-dot cell into a binary pattern.
// Bitwise Pattern Detection
byte pattern = 0;
for (int i=0; i<6; i++) {
if (digitalRead(btnPins[i]) == LOW)
pattern |= (1 << i); // Map buttons to binary bits
}
Lookup Table & Pattern Mapping
The brailleMap[] stores decimal equivalents of Braille dot patterns to match physical input to characters.
// Braille Lookup Table (A-Z)
const byte brailleMap[] = {
1, 3, 9, 25, 17, 11, 27, 19, 10, 26, // A-J
5, 7, 13, 29, 21, 15, 31, 23, 14, 30, // K-T
37, 39, 58, 45, 61, 53 // U-Z
};
Mode Logic: Alphabet vs. Number
// Mode Differentiation Logic
if (tR) detectedChar = brailleChars[i];
// Right touch = A-Z
else if (tL)
detectedChar = (i < 9) ? (i + 1) + '0' : '0';
// Left touch = 1-0
Touch Sensors:
• Left (tL): Number mode (1-0)
• Right (tR): Alphabet mode (A-Z)
• Both: Command confirmation

## Slide 8
Supported Commands & Feedback Patterns
Appliance Command Set
L1 / L2
Toggles light relays on Pins 13 and 12
Fxy
Controls Fan x (Room 1/2) at Speed y (0–4)
OPN
Rotates door servo to 90°; auto-closes after 5 seconds
ALL1 / ALL0
Master override for all devices
Command Parsing Implementation
if (inputBuffer == "L1") {
l1State = !l1State;
digitalWrite(RELAY_L1, l1State);
preferences.putBool("l1", l1State);
Blynk.virtualWrite(V1, l1State);
response = 'S';
}
else if (inputBuffer.startsWith("F")) {
int r = inputBuffer.charAt(1) - '0';
int s = inputBuffer.charAt(2) - '0';
if (r==1) { fan1State=s; setFan1Speed(s); }
}
Haptic & Audio Feedback Timing
The system ensures immediate confirmation for visually impaired users.
S
Success ('S')
400ms pulse for confirmed actions
E
Error ('E')
800ms long pulse for invalid commands
C
Correct Password ('C')
5 short pulses (400ms ON / 200ms GAP)
W
Wrong Password ('W')
5 long pulses (800ms ON / 200ms GAP)
Feedback Function Implementation
void triggerFeedback(char type) {
if (type == 'S') { // 400ms
digitalWrite(vibMotor, HIGH);
delay(400);
digitalWrite(vibMotor, LOW);
}
else if (type == 'C') { // 5× short
for (int i=0; i<5; i++) {
digitalWrite(vibMotor, HIGH);
delay(400);
digitalWrite(vibMotor, LOW);
if (i<4) delay(200);
}
}
}

## Slide 9
Capacitive Fan Regulator Design
Design Parameters
Load Analysis
Designed for a 33W load as it is listed under fan specifications.
Capacitor Selection
C₁ = 1.0µF and C₂ = 2.2µF (Non-polarized)
RC Time Constant Calculations (Discharge Safety)
Bleeder resistors (R = 470kΩ) are used for safety.
Step 1: Calculate τ (Tau)
For C₁ (1.0µF): τ = 470kΩ × 1.0µF = 0.47 seconds
For C₂ (2.2µF): τ = 470kΩ × 2.2µF = 1.03 seconds
Step 2: Safe Discharge Time (5τ)
Full discharge occurs after 5τ
C₁ Result: 0.47s × 5 = 2.35 seconds
C₂ Result: 1.03s × 5 = 5.15 seconds
Fan Speed Control Matrix
Speed | Relay 1 | Relay 2 | Relay 3 | Ceff
0 (OFF) | — | — | — | 0µF
1 (Low) | ON | — | — | 1.0µF
2 (Med-Low) | — | ON | — | 2.2µF
3 (Med-High) | ON | ON | — | 3.2µF
4 (Max) | — | — | ON | Bypass
Speed Control Implementation
void setFan1Speed(int speed) {
if (speed == 0) {
digitalWrite(RELAY_F1_1, RELAY_OFF);
digitalWrite(RELAY_F1_2, RELAY_OFF);
digitalWrite(RELAY_F1_3, RELAY_OFF);
} else {
digitalWrite(RELAY_F1_1,
(speed==1 || speed==3) ? RELAY_ON : RELAY_OFF);
digitalWrite(RELAY_F1_2,
(speed==2 || speed==3) ? RELAY_ON : RELAY_OFF);
digitalWrite(RELAY_F1_3,
(speed==4) ? RELAY_ON : RELAY_OFF);
}
Blynk.virtualWrite(V3, speed);
}
Resistors
R₁, R₃ = 220kΩ (¼W)
R₂, R₄ = 2.2Ω (1W)
Capacitors
C₁ = 1.0µF, 400V (cb22 105j400v)
C₂ = 2.2µF, 400V(cb22 225j400v)
Circuit diagram:
Relay 3
Relay 1
Relay 2
Load
(light /fan)

## Slide 10
IoT Integration & Safety Systems
Blynk Virtual Pin Mapping
The system syncs hardware states to the cloud for remote monitoring.
Virtual Pin | Device Assignment | Data Range
V1 | Light 1 Status | 0 (OFF) – 1 (ON)
V2 | Light 2 Status | 0 (OFF) – 1 (ON)
V3 | Fan 1 Speed | 0 – 4
V4 | Fan 2 Speed | 0 – 4
Blynk Synchronization Code
// Hardware → Cloud (State Updates)if(Blynk.connected()) {
Blynk.virtualWrite(V1, l1State);
Blynk.virtualWrite(V2, l2State);
Blynk.virtualWrite(V3, fan1State);
Blynk.virtualWrite(V4, fan2State);
}
// Cloud → Hardware (Control Commands)
BLYNK_WRITE(V1) {
l1State = param.asInt();
digitalWrite(RELAY_L1, l1State);
}
Safety System Logic
Fire Detection
Flame sensor on Pin 4 detects hazards and triggers alerts every 1000ms.
Human-in-the-Loop Verification
ACK (Both Sensors): Confirms emergency, opens door, and sends Blynk notification
STOP (One Sensor): False alarm cancellation
Validation
User must hold sensor(s) for 2000ms to prevent accidental triggers.
Emergency Response Implementation
// Fire Detection Loop (Active HIGH)if (digitalRead(FLAME_PIN) == HIGH) {
if (!fireActive) {
fireActive = true;
updateOled("!! FIRE !!");
}
if (millis() - lastFireMsg > 1000) {
lastFireMsg = millis();
activeClient.print('F'); // Alert remote
}
}
// ACK: Confirmed Emergencyif (inputBuffer == "ACK") {
fireActive = false;
doorServo.write(90); // Open door
Blynk.logEvent("fire_alert",
"Fire Alarm Confirmed!");
}
Password Logic ("1010"): Touch + button → “1” otherwise “0”2-second hold on the button clears the input while long touch on touch sensor submits the password.
Table 10: Blynk IoT integration and safety system architecture
Braille-Based IoT Home Automation