## Slide 1
Braille-Based IoT Home Automation for
Multi-Disability Empowerment
SESHADRI RAO GUDLAVALLERU ENGINEERING COLEGE
(An Autonomous Institute permanently affiliated to JNTUK , Kakinada)
Department of Electronics and Communication Engineering
Batch Members:
N. Manikanta Raghava — 23485A0424
M. Jahnavi — 22481A04F5
N. Venkata Siva Prasanth — 23485A0423
Md. Habeeb Pasha — 22481A04F8
Guided by:
Mr. V. Vittal Reddy
(Associate Professor)
Batch No : C5

## Slide 2
Objectives of the Project Work
Develop a low-cost, accessible Braille-based IoT system that empowers visually and speech-impaired individuals to control home appliances independently, providing real-time confirmation through haptic feedback and audio signals to ensure accuracy and ease of use.
Implement an intelligent emergency alert system that detects hazards like fire and instantly notifies caregivers via Blynk IoT cloud push notifications ensuring continuous safety and reliability during critical situations.

## Slide 3
Abstract of the Project Work
This project presents a Braille-based IoT home automation system designed to assist visually and speech-impaired individuals. Built on ESP32 microcontrollers, the system employs a custom persistent TCP protocol to transmit commands from a portable six-dot Braille keypad to a central appliance controller. Accessibility is ensured through simultaneous haptic (vibration) and auditory feedback for the user, while an SSD1306 OLED display provides visual status for caregivers. Additionally, the system integrates flame sensors and Blynk IoT connectivity to provide real-time safety alerts, offering a secure, reliable, and inclusive alternative to conventional smart home controls.

## Slide 4
Hardware Wiring Diagram
Remote Module

## Slide 5
Hardware Wiring Diagram
Appliance Control Module

## Slide 6: Flow chart
Power ON
Initialize sensors & Wi-Fi
Read inputs
Send ACK or STOP
Send appliance command
Is Feedback Received from TCP
Play Feedback
Power ON
Initialize sensors, Wi-Fi & Display
Listen TCP for commands
Emergency alert
Decode command
Is Command Received
Update display
Execute command & give Feedback
Is Flame detected
Monitor Flame sensor
Braille Keypad Module
Appliance Control Module
Valid Braille Input
Emergency
Yes
Yes
Yes
No
No
No
‘F’ fire alert
feedback pattern →
S/E/C/W
feedback pattern →

## Slide 7
SYSTEM ARCHITECTURE
The Handshake: Master/Slave Model
Communication Protocol
01
Master/Slave Architecture
Remote Module (TCP Client) → Appliance Module (TCP Server)
02
WiFi Mode: WIFI_AP_STA
Dual-mode operation for flexible network configuration
03
TCP Communication Port 7890
Reliable connection-oriented protocol for command transmission
Key Code Implementation
WiFiServer tcpServer(7890);
WiFiClient activeClient;
// Server initialization in setup()
tcpServer.begin();
// Client connection handling in loop()
if (tcpServer.hasClient()) {
activeClient = tcpServer.available();
}
Network Topology
Remote Module
TCP Client
Braille Input • Haptic Output
TCP Port 7890
Appliance Module
TCP Server
Relay Control • IoT Integration
Network SSID
ESP32-Server
Password
12345678

## Slide 8
REMOTE MODULE
Input Logic: The Braille Engine
Hardware Input System
6
Braille Pushbuttons
btnPins[] array
Six buttons arranged in standard Braille cell pattern (2 columns × 3 rows). Each button represents one dot position.
2
Touch Sensors
touchLeft & touchRight
TTP223 capacitive touch sensors for mode selection and command confirmation.
Bitwise Pattern Detection
// Read 6 buttons into binary pattern (Lines 206-209)
byte pattern = 0;
for (int i=0; i<6; i++) {
if (digitalRead(btnPins[i]) == LOW)
pattern |= (1 << i);
}
Mode Differentiation Logic
Left Touch + Pattern = Number Mode
When left touch sensor is activated during button press, pattern maps to digits 1-0 (A-J patterns).
detectedChar = (i < 9) ? (i + 1) + '0' : '0'
Right Touch + Pattern = Alphabet Mode
When right touch sensor is activated, pattern maps to letters A-Z using brailleMap[] lookup table.
detectedChar = brailleChars[i]
Braille Lookup Table
// brailleMap[] array (Lines 29-33)
const byte brailleMap[] = {
1, 3, 9, 25, 17, 11, 27, 19, 10, 26, // A-J
5, 7, 13, 29, 21, 15, 31, 23, 14, 30, // K-T
37, 39, 58, 45, 61, 53// U-Z
};

## Slide 9
HAPTIC & AUDIO INTERFACE
Feedback Systems
Feedback Function Implementation
voidtriggerFeedback(char type) {
if (type == 'S') { // Success - 400ms
digitalWrite(vibMotor, HIGH);
digitalWrite(buzzer, HIGH);
delay(400);
digitalWrite(vibMotor, LOW);
digitalWrite(buzzer, LOW);
}
else if (type == 'E') { // Error - 800ms
// Long vibration/beep pattern
delay(800);
}
else if (type == 'C') { // Correct Password - 5× short
for (int i=0; i<5; i++) {
// 400ms ON, 200ms OFF × 5
}
}
}
Hardware Pin Configuration
Vibration Motor
Pin 12
NPN transistor driver (2N2222) with 1kΩ base resistor and 1N4007 flyback diode
Buzzer
Pin 25
Active piezo buzzer for audio feedback synchronized with vibration
Feedback Patterns
S
Success
400ms short vibration/beep
E
Error
800ms long vibration/beep
F
Fire Emergency
Continuous loop until ACK/STOP
C
Correct Password
5× short beeps/vibrations
W
Wrong Password
5× long beeps/vibrations
Design Principle: Non-visual interaction ensuring visually impaired users receive immediate tactile and auditory confirmation of all system actions.

## Slide 10
SAFETY SYSTEM
Emergency Detection Logic (Client Side)
Emergency Trigger Mechanism
1. Fire Detection Signal
Server sends character 'F' when flame sensor detects fire. Client immediately enters emergencyMode .
2. Continuous Alert Pattern
System generates continuous short beeps/vibrations (400ms ON, 600ms OFF) until user responds.
3. User Response Window
System monitors touch sensors for user confirmation within configurable timeout period.
Emergency Mode Entry
// Lines 114-120: Fire alert detection
if (c == 'F') {
emergencyMode = true;
emergencyTimer = millis();
}
// Lines 127-137: Continuous alert pattern
if (millis() - emergencyTimer > 1000) {
digitalWrite(vibMotor, HIGH);
digitalWrite(buzzer, HIGH);
delay(400);
// ... alternating pattern
}
User Response Logic
False Alarm
Hold ONE touch sensor
tcpClient.print("STOP\n")
Sends STOP command to cancel alert without triggering Blynk notification
OR
Real Emergency
Hold BOTH touch sensors
tcpClient.print("ACK\n")
Sends ACK command confirming emergency, triggers Blynk notification
2-Second Validation
Code Line 314: User must hold sensor(s) for 2000ms to prevent accidental triggers

## Slide 11
APPLIANCE MODULE
The Control Hub (Server Side)
TCP Server Implementation
// Line 278: Server initialization
WiFiServer tcpServer(7890);
WiFiClient activeClient;
// Lines 445-454: Client connection handling
if (tcpServer.hasClient()) {
if (activeClient && activeClient.connected()) {
// Reject new connection if one active
WiFiClient newClient = tcpServer.available();
newClient.stop();
} else {
activeClient = tcpServer.available();
}
}
Command Parsing Loop
// Lines 455-563: Main command processing
if (activeClient && activeClient.connected()) {
while (activeClient.available()) {
char c = activeClient.read();
if (c == '\n') {
inputBuffer.trim();
lastCommand = inputBuffer;
// Parse and execute command...
activeClient.print(response);
} else {
inputBuffer += c;
}
}
}
Global State Variables
bool l1State, l2State
Light relay states (true=ON, false=OFF)
int fan1State, fan2State
Fan speed levels (0-4, where 0=OFF)
String lastCommand
Most recently executed command
bool fireActive
Emergency state flag
Response Codes
S
Command executed successfully
E
Invalid command or error

## Slide 12
COMMUNICATION PROTOCOL
Text-to-Action Command Mapping
Command Structure
L1, L2
Light Control
Toggle light relays on Pins 13 (L1) and 12 (L2)
l1State = !l1State;
digitalWrite(RELAY_L1, l1State ? RELAY_ON : RELAY_OFF);
preferences.putBool("l1", l1State);
Fxy
Fan Control
x = Room (1,2), y = Speed (0-4)
int r = inputBuffer.charAt(1) - '0';
int s = inputBuffer.charAt(2) - '0';
if (r==1) { fan1State=s; setFan1Speed(s); }
Complete Command Reference
L1
Toggle Light 1 (Pin 13)
L2
Toggle Light 2 (Pin 12)
F11
Fan 1, Speed 1 (Low)
F24
Fan 2, Speed 4 (Max)
ALL1
Master ON (All devices)
ALL0
Master OFF (All devices)
OPN
Open Door (Servo 90°)
Door Control (Line 688)
else if (inputBuffer == "OPN") {
doorServo.write(90);
doorOpenTime = millis();
doorAutoClose = true;
response = 'S';
}
Auto-closes after 5 seconds (Line 437-443)
Blynk Synchronization
// Lines 469, 477: Update Blynk virtual pins
if(Blynk.connected())
Blynk.virtualWrite(V1, l1State);
Blynk.virtualWrite(V2, l2State);
Blynk.virtualWrite(V3, fan1State);

## Slide 13
CAPACITOR BANK CONTROL
Fan Speed Logic
Hardware Implementation
Uses 3 relays per fan for speed regulation via capacitor switching (not PWM). This method provides smoother speed control for AC induction motors.
Relay 1
1.0µF Cap
Relay 2
2.2µF Cap
Relay 3
Direct
setFan1Speed Function (Lines 351-362)
voidsetFan1Speed(int speed) {
if (speed == 0) {
// All relays OFF
digitalWrite(RELAY_F1_1, RELAY_OFF);
digitalWrite(RELAY_F1_2, RELAY_OFF);
digitalWrite(RELAY_F1_3, RELAY_OFF);
} else {
// Speed 1-4 logic
digitalWrite(RELAY_F1_1, (speed==1 || speed==3) ? RELAY_ON : RELAY_OFF);
digitalWrite(RELAY_F1_2, (speed==2 || speed==3) ? RELAY_ON : RELAY_OFF);
digitalWrite(RELAY_F1_3, (speed==4) ? RELAY_ON : RELAY_OFF);
}
}
Speed Level Matrix
Speed | C1 | C2 | C_eff
0 (OFF) | 1.0µF | 2.2µF | 0µF
1 (Low) | 1.0µF | 2.2µF | 1.0µF
2 (Med-Low) | 1.0µF | 2.2µF | 2.2µF
3 (Med-High) | 1.0µF | 2.2µF | 3.2µF
4 (Max) | 1.0µF | 2.2µF | Bypass
Circuit diagram of RC fan regulator
load
Relay 3
Relay 1
Relay 2

## Slide 14
SAFETY SYSTEM
Fire Safety State Machine
Three-State Safety System
1
Detection
IR Flame Sensor (Pin 4)
Sensor detects fire (Active HIGH), sets fireActive = true, sends 'F' to Remote Module every 1000ms.
2
Awaiting Confirmation
Human-in-the-Loop
Blocks other inputs until "ACK" or "STOP" received from user via touch sensors.
3
Action (On ACK)
Emergency Response
Opens door (Servo 90°), triggers Blynk notification, displays "Alert Confirmed" on OLED.
Fire Detection Loop (Lines 638-647)
if (digitalRead(FLAME_PIN) == HIGH) {
if (!fireActive) {
fireActive = true ;
updateOled( "!! FIRE !!" );
}
if (millis() - lastFireMsg > 1000 ) {
lastFireMsg = millis();
activeClient.print( 'F' );
}
}
State Transition Diagram
IDLE
Normal Operation
DETECTION
Fire Detected → Send 'F'
Any touch
AWAITING
Wait for ACK/STOP
ACK
STOP
CONFIRMED
Blynk + Door
CANCELLED
Silent Stop
Safety-First Design
The human-in-the-loop verification prevents false IoT alerts due to sensor errors or transient conditions. Emergency notifications are only sent after explicit user confirmation.

## Slide 15
HYBRID INPUT SYSTEM
Manual "Smart Button" Logic
Dual-Mode Button Operation
Short Press
< 500ms
Toggles device ON/OFF. If fan is running, saves current speed to savedFan variable before turning off.
Long Press
> 500ms
Cycles through speed levels: 1 → 2 → 3 → 4 → 1. Implements 500ms interval between speed changes.
Debouncing Implementation
// Lines 649-686: Fan button with debounce
if (f1Btn == LOW && lastBtn1State == HIGH) {
btn1PressStart = millis();
btn1Active = true;
}
if (f1Btn == LOW && btn1Active) {
if (millis() - btn1PressStart > 500) {
// Long press detected
btn1LongPress = true;
}
}
State Management Variables
unsigned long btn1PressStart
Records button press start time for duration calculation
bool btn1Active
Tracks if button is currently being pressed
bool btn1LongPress
Flags long press to prevent toggle on release
int savedFan1
Stores last speed setting for resume functionality
unsigned long lastFan1Change
500ms interval timer between speed increments
Speed Cycling Logic
if (fan1State == 0) fan1State = 1;
else {
fan1State++;
if (fan1State > 4) fan1State = 1;
}

## Slide 16
ACCESS CONTROL
Security System – The "1010" Logic
Two-Input Binary Entry System
Button (Pin 5)
Data Bit
Pressed = 1
Released = 0
Touch (Pin 23)
Clock/Enter
Short = Bit Entry
Long = Submit
User enters binary password by holding button (for '1') or releasing (for '0'), then tapping touch sensor to clock in each bit. Long press on touch submits password for validation.
Password Validation (Lines 614-625)
const String CORRECT_PASSWORD = "1010";
if (passInput == CORRECT_PASSWORD) {
updateOled("Access\nGRANTED");
activeClient.print('C'); // Send correct feedback
passInput = "";
} else {
updateOled("Access\nDENIED");
activeClient.print('W'); // Send wrong feedback
passInput = "";
}
Password Entry Flow
1
Enter Bit
Hold button for '1', release for '0'
2
Clock Bit
Short tap touch sensor (<1s)
3
Repeat
Continue for all 4 bits
4
Submit
Long press touch (>2s)
Example: 1-0-1-0 = Access Granted
Haptic Feedback Response
C
Correct
5 short beeps/vibrations
W
Wrong
5 long beeps/vibrations

## Slide 17
CLOUD CONNECTIVITY
IoT Integration (Blynk Cloud)
Blynk Library Integration
// Lines 243-245: Blynk configuration
#define BLYNK_TEMPLATE_ID "TMPL3VTwLUsho"
#define BLYNK_TEMPLATE_NAME "BRAILLE ASSISTIVE HOME"
#define BLYNK_AUTH_TOKEN "xFRDYtkIVA-pcnq9-d_y8FMOUg57N_j2"
#include
Blynk is a low-code IoT platform trusted by 5,000+ companies and over 1 million developers worldwide.
Bidirectional Data Sync
// Hardware → App (Lines 361, 469, 477)
Blynk.virtualWrite(V1, l1State);
Blynk.virtualWrite(V3, fan1State);
// App → Hardware (Blynk handlers)
BLYNK_WRITE(V1) {
l1State = param.asInt();
digitalWrite(RELAY_L1, l1State);
}
Virtual Pin Mapping
V1
Light 1 State
Boolean (0/1)
V2
Light 2 State
Boolean (0/1)
V3
Fan 1 Speed
Integer (0-4)
V4
Fan 2 Speed
Integer (0-4)
Critical Push Notification
// Line 717: Fire alert notification
if(Blynk.connected()) {
Blynk.logEvent("fire_alert",
"Fire Alarm Confirmed by User!");
}
Safety Feature: Notification only triggers on user-confirmed emergency (ACK), preventing false alarms.

## Slide 18
USER INTERFACE
OLED Display Management
Adafruit SSD1306 Library
#include
// Display initialization (Line 281)
Adafruit_SSD1306 display(128, 64, &Wire, -1);
// I2C pins (Lines 265-266)
#define OLED_SDA 21
#define OLED_SCL 22
128×64 pixel monochrome OLED display provides visual feedback for sighted caregivers and debugging information.
showStatus Function (Lines 328-348)
voidshowStatus() {
display.clearDisplay();
display.setTextSize(2);
display.setTextColor(WHITE);
// Line 1: Last Command
display.setCursor(0, 0);
display.print("CMD:");
display.println(lastCommand.substring(0,5));
// Line 2: Light Status
display.print("L1:"); display.print(l1State);
display.print(" L2:"); display.println(l2State);
// Line 3: Fan Status
display.print("F1:"); display.print(fan1State);
display.print(" F2:"); display.println(fan2State);
display.display();
}
Dynamic UI Layout
1
Line 1: Last Received Command (truncated to 5 chars)
2
Line 2: Light States (L1, L2: 0=OFF, 1=ON)
3
Line 3: Fan Speeds (F1, F2: 0-4)
Special Display Modes
Fire Emergency
Displays "!! FIRE !!"
Password Entry
Shows "PW: 101" as typed
CMD: L1
L1: 1 L2: 0
F1: 4 F2: 2

## Slide 19
FLASH STORAGE
Data Persistence (Preferences)
The Problem
Power loss resets all relay states. Without persistence, all lights and fans return to OFF after power restoration, disrupting user experience and requiring manual reconfiguration.
Power Loss
All states lost
After Reset
Defaults restored
Save State (On Change)
// Lines 468, 476: Save light states
preferences.putBool("l1", l1State);
preferences.putBool("l2", l2State);
// Lines 485, 490: Save fan states
preferences.putInt("f1", fan1State);
preferences.putInt("f2", fan2State);
The Solution
ESP32 Preferences.h library provides non-volatile storage (NVS) in flash memory. Data persists across resets and power failures.
#include
Preferences preferences;
// Initialize namespace (Line 410)
preferences.begin("home_auto", false);
Restore State (On Boot)
// Lines 411-414: Restore from flash
l1State = preferences.getBool("l1", false);
l2State = preferences.getBool("l2", false);
fan1State = preferences.getInt("f1", 0);
fan2State = preferences.getInt("f2", 0);
// Apply restored states (Lines 417-420)
digitalWrite(RELAY_L1, l1State ? RELAY_ON : RELAY_OFF);
setFan1Speed(fan1State);
Namespace: "home_auto" | Data Types: bool, int, String | Max Key Length: 15 characters

## Slide 20
CONCLUSION
Summary & Project Impact
Code Efficiency
Non-blocking architecture using millis() enables multitasking without interrupt delays.
Button debouncing
Emergency timers
WiFi reconnection
Speed cycling intervals
Accessibility
Converts binary physical inputs into complex TCP command strings, enabling independent home control for visually impaired users.
Standard Braille input
Haptic & audio feedback
Mode differentiation
Non-visual interface
Safety
Human-in-the-loop verification for fire alarms prevents false IoT alerts and ensures reliable emergency response.
2-second validation
ACK/STOP confirmation
Automatic door opening
Blynk push notifications
A Robust Dual-Module System
Bridging Braille physical inputs with modern IoT infrastructure, demonstrating how embedded systems engineering can enhance independence and quality of life for visually impaired users.
2
ESP32 Modules
15
Commands
5
Feedback Types